## Slide 1: Machine-Level Programming : Basics

## Slide 2: Goals of Lecture
Programming Languages
  Between high-level language and machine code
  Why learn assembly-language programming?
Computer architecture
  History of Intel processors and architectures
  Central Processing Unit (CPU)
  Fetch-decode-execute cycle
C code vs. assembly code
  Small IA32 example to illustrate the relationship to C
  C, assembly, machine code

## Slide 3: Programming Languages

## Slide 4: Programming Languages
Hardware
Machine Code
Assembly Language
High Level Language

## Slide 5: High-Level Language
Make programming easier by describing operations in a natural language
Increase the portability of the code
One line may involve many low-level operations
Examples: C, C++, Java, Pascal, …
count = 0;
while (n > 1) {
count++;
if (n & 1)
n = n*3 + 1;
else
n = n/2;
}

## Slide 6: Compiler
A program written in a high level language may be translated to machine code using a compiler.
Compiler
cmp esi,0
jne .L1
add esi,5
.L1
if(x == 0)
x = x + 5;
Assembler
0x81FE00000000
0x7506
0x81C605000000

## Slide 7: Machine Language
Lowest level programming language.
Each CPU instruction is represented as an opcode, which is an unsigned integer number.
Only language that the computer really understands.
Difficult to understand by human beings.

## Slide 8: Machine Language
Tied to the underlying machine
What the computer sees and deals with
Every command is a sequence of one or more numbers
All stored in memory on the computer, and read and executed
0000 0000 0000 0000 0000 0000 0000 0000
0000 0000 0000 0000 0000 0000 0000 0000
9222 9120 1121 A120 1121 A121 7211 0000
0000 0001 0002 0003 0004 0005 0006 0007
0008 0009 000A 000B 000C 000D 000E 000F
0000 0000 0000 FE10 FACE CAFE ACED CEDE
1234 5678 9ABC DEF0 0000 0000 F00D 0000
0000 0000 EEEE 1111 EEEE 1111 0000 0000
B1B2 F1F5 0000 0000 0000 0000 0000 0000

## Slide 9: Machine Code Example
The opcode for adding one to the accumulator in the Intel x86 is:
01000000b
or
0x40

## Slide 10: Assembly Language
Same instruction set as machine code.
Each opcode is replaced by a symbolic name.
Less cryptic for human beings.

## Slide 11: Assembly Language
Tied to the specifics of the underlying machine
Commands and names to make the code readable and writeable by humans
E.g., IA32 from Intel
movl %edx, %eax
andl $1, %eax
je .else
jmp .endif
.else:
.endif:
sarl $1, %edx
movl %edx, %eax
addl %eax, %edx
addl %eax, %edx
addl $1, %edx
addl $1, %ecx
.loop:
cmpl $1, %edx
jle .endloop
jmp .loop
.endloop:
movl $0, %ecx

## Slide 12: Assembly Language Example
The Intel x86 assembly language instruction that adds one to the accumulator is:
inc eax

## Slide 13: Assembler
In order to execute a program written in assembly language, it first has to be translated to machine code using a special program called an assembler.
Assembler
0x40
inc eax

## Slide 14: Reasons for Studying Assembly Language
To understand some of the low level details of how a real computer operates.
To get to know some technologies that can only be understood using assembly language.
To obtain a better appreciation of the inner-workings of a compiler.

## Slide 15: Why Learn Assembly Language?
Write faster code
  By understanding which high-level constructs are better
  … in terms of how efficient they are at the machine level
Small executable code
Understand how things work underneath
  Learn the basic organization of the underlying machine
  Learn how the computer actually runs a program
Some software is still written in assembly language
  Code that really needs to run quickly
  Code for embedded systems, network processors, etc.

## Slide 16: Assembly Language Disadvantages
Error prone.
Long and tedious to write.
Difficult to understand and modify.
Strongly tied to a specific computer architecture.

## Slide 17: Intel x86 Processors

## Slide 18: RISC: Reduced Instruction Set Computer
Microprocessor that uses a relatively small number of fast but simple instructions.
Cheaper to design and produce because they require less transistors.
Mainly used in workstations.

## Slide 19: CISC: Complex Instruction Set Computer
Microprocessor that uses a significantly large amount of complex (specialized) instructions.
Mainly used for Intel’s x86 architecture.

## Slide 20: Intel x86 Processors
Dominate laptop/desktop/server market
Evolutionary design
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time goes on
Complex instruction set computer (CISC)
  Many different instructions with many different formats
    But, only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)

## Slide 21: Intel x86 Evolution: Milestones
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit Intel processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32 bit Intel processor , referred to as IA32
  Added “flat addressing”, capable of running Unix
Pentium 4F 2004 125M 2800-3800
  First 64-bit Intel processor, referred to as x86-64
Core 2 2006 291M 1060-3500
  First multi-core Intel processor
Core i7 2008 731M 1700-3900
  Four cores (most office and lab machines)

## Slide 22: Intel x86 Processors, cont.
Machine Evolution
  386 1985 0.3M
  Pentium 1993 3.1M
  Pentium/MMX 1997 4.5M
  PentiumPro 1995 6.5M
  Pentium III 1999 8.2M
  Pentium 4 2001 42M
  Core 2 Duo 2006 291M
  Core i7 2008 731M
Added Features
  Instructions to support multimedia operations
  Instructions to enable more efficient conditional operations
  Transition from 32 bits to 64 bits
  More cores

## Slide 23: Our Coverage
IA32
  The traditional x86
  ubuntu@ubuntu> gcc –m32 hello.c
x86-64
  The emerging standard
  ubuntu@ubuntu> gcc hello.c
  ubuntu@ubuntu> gcc –m64 hello.c
Presentation
  Book presents IA32 in Sections 3.1—3.12
  Covers x86-64 in 3.13
  We will cover both simultaneously

## Slide 24: Why Learn Intel IA32 Assembly?
Program natively on our computing platform
  Rather than using an emulator to mimic another machine
Learn instruction set for the most popular platform
  Most likely to work with Intel platforms in the future
But, this comes at some cost in complexity
  IA32 has a large and varied set of instructions
  Arguably more than are really useful in practice

## Slide 25: Computer Architecture

## Slide 26: Definitions
Architecture: (also ISA: instruction set architecture) The parts of a processor design that one needs to understand to write assembly code.
  Examples: instruction set specification, registers.
Microarchitecture: Implementation of the architecture.
  Examples: cache sizes and core frequency.
Example ISAs (Intel): IA32, x86-64

## Slide 27: Von Neumann Architecture
Central Processing Unit
  Control unit
    Fetch, decode, and execute
  Arithmetic and logic unit
    Execution of low-level operations
  General-purpose registers
    High-speed temporary storage
  Data bus
    Provide access to memory
Memory
  Store instructions
  Store data
Random Access
Memory (RAM)
Control
Unit
ALU
CPU
Registers
Data bus

## Slide 28: Assembly Programmer’s View
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “EIP” (IA32) or “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte addressable array
    Code and user data
    Stack to support procedures

## Slide 29: CPU Instructions
Each instruction has:
  an opcode (operation code), that indicates which operation to perform.
  zero or more operands, which may be
    registers,
    constants or
    memory locations.

## Slide 30: Fetch-Execute Cycle
Fetch:
  1. Fetch an instruction from memory.
  2. Decode the instruction to determine the operation.
  3. Fetch data from memory if necessary.
Execute:
  4. Perform the operation on the data.
  5. Store the result in memory if needed.

## Slide 31: Control Unit: Instruction Pointer
Stores the location of the next instruction
  Address to use when reading from memory
Changing the instruction pointer (EIP)
  Increment by one to go to the next instruction
  Or, load a new value to “jump” to a new location
EIP

## Slide 32: Control Unit: Instruction Decoder
Determines what operations need to take place
  Translate the machine-language instruction
Control what operations are done on what data
  E.g., control what data are fed to the ALU
  E.g., enable the ALU to do multiplication or addition
  E.g., read from a particular address in memory
ALU

## Slide 33: Registers
Small amount of storage on the CPU
  Can be accessed more quickly than main memory
Instructions move in and out of registers
  Loading registers from main memory
  Storing registers to main memory
Instructions manipulate the register contents
  Registers essentially act as temporary variables
  For efficient manipulation of the data
Registers are the top of the memory hierarchy
  Ahead of cache, main memory, disk, tape, …

## Slide 34: Turning C into Object Code
text
text
binary
binary
Compiler (gcc -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –O1 p1.c p2.c -o p
    Use basic optimizations (-O1)
    Put resulting binary in file p

## Slide 35: Compiling Into Assembly
C Code (p1.c)
int sum(int x, int y)
{
int t = x+y;
return t;
}
Generated IA32 Assembly
sum:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
addl 8(%ebp),%eax
popl %ebp
ret
Obtain with command
  gcc –O1 –m32 –S p1.c
Produces file p1.s
Warning: Will get very different results on different machines due to different versions of gcc and different compiler settings.

## Slide 36: Object Code
Code for sum
0x08483f4 <sum>:
0x55
0x89
0xe5
0x8b
0x45
0x0c
0x03
0x45
0x08
0x5d
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 11 bytes
  Each instruction 1, 2, or 3 bytes
  Starts at address 0x08483f4

## Slide 37: Machine Instruction Example
C Code
  Add two signed integers
Assembly
  Add two 4-byte integers
    “Long” words in GCC parlance
    Same instruction whether signed or unsigned
  Operands:
    x: Register %eax
    y: Memory M[%ebp+8]
    t: Register %eax
      Return function value in %eax
Object Code
  3-byte instruction
  Stored at address 0x80483fa
int t = x+y;
addl 8(%ebp),%eax
0x80483fa: 03 45 08
Similar to expression:
x += y
More precisely:
int eax;
int *ebp;
eax += ebp[2]

## Slide 38: Disassembling Object Code
Disassembled
Disassembler
  objdump -d p
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
080483f4 <sum>:
80483f4: 55 push %ebp
80483f5: 89 e5 mov %esp,%ebp
80483f7: 8b 45 0c mov 0xc(%ebp),%eax
80483fa: 03 45 08 add 0x8(%ebp),%eax
80483fd: 5d pop %ebp
80483fe: c3 ret

## Slide 39: Alternate Disassembly
Disassembled
Dump of assembler code for function sum:
0x080483f4 <sum+0>: push %ebp
0x080483f5 <sum+1>: mov %esp,%ebp
0x080483f7 <sum+3>: mov 0xc(%ebp),%eax
0x080483fa <sum+6>: add 0x8(%ebp),%eax
0x080483fd <sum+9>: pop %ebp
0x080483fe <sum+10>: ret
Within gdb Debugger
Compile using
gcc p1.c -g –o p
  gdb p
  disassemble sum
  Disassemble procedure
Object
0x080483f4:
0x55
0x89
0xe5
0x8b
0x45
0x0c
0x03
0x45
0x08
0x5d
0xc3

## Slide 40: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91